## Slide 1: Is Prefetcher Research Still Alive?
Data Prefetching Championship #4
Leeor Peled, CPU uArch Research, Huawei
Jan 2026

## Slide 2: Short bio 
PhD at the Technion under Prof. Uri Weiser & Prof. Yoav Etsion) focused on ML based prefetchers with rich context (Q-learning, bandits, Neural networks, LSTM)
20+ years doing CPU core architecture
  Intel Haifa: working on various core clusters (FE, OOO, HWPF, L2) for Sandybrige, Ivybridge, Skylake, Cannonlake, Icelake (Sunnycove), Alderlake (Goldencove), Meteorlake (Redwoodcove)…
  Huawei Israel: working on cores for Mobile phones (Huawei Mate), server CPUs (Kunpeng) and other domains.
Currently: Huawei, leading CPU architecture research (Israel, Zurich, Cambridge, Edinburgh, and China)
  Prefetchers, Predictors, Parallelism, Caches, SW/HW codesign, System/OS, Dynamic optimization, Compilers, Power efficiency, …
HUAWEI

## Slide 3
Huawei: A Global Provider of ICT Infrastructure and Smart Devices
Bring digital to every person, home and organization for a fully connected, intelligent world
Huawei's end-to-end portfolio of products, solutions and services are both competitive and secure. Through open collaboration with ecosystem partners, we create lasting value for our customers, working to empower people, enrich home life, and inspire innovation in organizations of all shapes and sizes.
At Huawei, innovation focuses on customer needs. We invest heavily in basic research, concentrating on technological breakthroughs that drive the world forward.
207,000
Employees
55.4%
R&D employees
Rank 4th
Global R&D investment
170+
Countries and regions

## Slide 4: The memory wall (because we always start there)
Memory performance is not scaling as fast as needed!
Cache hierarchy offers some mitigation, but not enough
Will further degrade with core count, remote mem, networks, warehouse scale etc…
BW can be somewhat mitigated, but at a further cost for latency
  So, we prefetch…
Deep-dive Analysis of the Data Analytics Workload in CloudSuite
Yasin et al. [IISWC 2014]
Computer Architecture: A Quantitative Approach]
[Hennessy & Patterson
Gap
50% per year
Ayar labs

## Slide 5: Related work per year
Source: Google scholar stats
Technical Report: Prefetching for complex memory access patterns. Sam Ainsworth, 2018
Chart: Prefetching papers per year
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024
count | 27 | 32 | 54 | 58 | 59 | 72 | 79 | 123 | 175 | 160 | 235 | 253 | 304 | 457 | 533 | 672 | 706 | 813 | 810 | 840 | 979 | 978 | 1020 | 1120 | 1380 | 1520 | 1420 | 1550 | 1470 | 1590 | 1600 | 1590 | 1640 | 1760 | 1700 | 1780 | 1670 | 1600 | 1750 | 1760 | 1740 | 1740 | 1790 | 1800 | 1990
#
year

## Slide 6: Designing prefetchers in 2026, still relevant?
BORN JUST IN TIME TO DESIGN THE BEST PREFETCHER EVER???
Is there still something to discover?
(Bonus question: Is it still possible to get a paper accepted?)

## Slide 7: Brief history (non-exhaustive)
Spatial
  Next line
  Streaming prefetchers
  Stride prefetchers
  Alternating strides
  Signature-based strides
Next stop: Irregular?…
SMS
GHB G/AC
GHB G/DC
SPP
Temporal
  Early temporal (Markov)
  History based (GHB-like)
  Storage /optimization
  Contextual correlations
Spatio-temporal
  Recurring Deltas
  Recurring patterns
  Correlated patterns

## Slide 8: Irregular patterns
Horrible name, definition by negation!
  What makes these patterns not regular?
Some examples
  pointer chasing schemes
    Linked lists
    Skip lists / Jump pointers
  Arrays of pointers
  Arrays of indices
    CSR/CSC
    Graphs (optimized)
  Linked data structures
  Complex / H2P traversal algorithms
  Random walks
Common idioms
[Roth & Sohi, Jump pointers, 99]

## Slide 9: Why are we here?
Science advances by either isolating a problem and solving it, or, once reaching saturation, by shifting the paradigm/perspective to create new problems.
  Everything besides that is engineering.
  If you don’t see a huge fundamental problem in front of you, reconsider your perspective.
In the context of prefetching:
  Problem: need to predict next addresses in advance
  Solution: detect and apply address patterns that conform with // sequences, strides
    Optimization: lookahead
  Saturation: some patterns do not conform with a fixed function relation, still seeing misses  new problem
  Solution: add temporal correlations storage: // can store addresses, delta, patterns, …
  Solution #2: add history: // covers alternating strides,
  Saturation: some workloads have combined patterns. New problem.
  Solution #3: ensemble of prefetchers:
Still not enough… now what?
  Option 1: move from function (memorization of spatio-temporal patterns) to compute
    “Semantic correlation”
    Runahead prefetchers already started, but can we do better?
  Option 2: better learning model for more complex patterns
    NN based prefetching can help. Can it also generate previously unseen
    addresses/patterns?
Problem
Solution
Saturation
Shift

## Slide 10: What’s left?
Complex patterns: what makes them so?
  x = A(hash[i]) ;
  x = xptr1ptr2;
  x = cond? y : z;
Find better temporal correlations
  How can we record only the relevant relations?
  How can we trigger only the correct correlations?
  Untangling interleaved streams
Multilevel prefetching
  Orchestrate timeliness (L123 done, what rack scale (net/ storage)?)
Multicore fairness
  Avoid all-or-none throttling on symmetric cases
  Divide the cache and BW resources based on who may benefit the most?
    NP hard even if we knew the future benefit (which we don’t..)
    Speculate benefits, approximate optimal distribution
Specialized workloads
  AI tiling, token reuse, weight reuse
  Raytracing, Databases, KV caches
ML based prefetching
  RL based techniques already proposed for action learning
    MAB / Context bandits / Pythia
  Can we generate addresses directly using ML/DL?
    Bit level / offsets / embedding / something else?
Do we (finally) join the LLM wagon?
  LLMs train over large text sequences
    Attention based models help us find optimal context
  Can we use memory traces (possibly augmented with further context) are input streams?
  Feed them onto an offline model, let it learn the probability
  Let the attention scheme work its magic
  …
  Profit?
But..
  What’s the use of an offline model?
  Find a way to distill the model learning and extract insights on previously unseen pattern
  … or just ask the model to build you a prefetcher and look for a new job.
How do we generalize?
B D
C
A

## Slide 11: Questions?

## Slide 12: Performance bottlenecks in modern CPUs (and some mitigations)
What else?
Additional domains (SoC, MC, networking, storage,…)
System level behavior
Dedicated workloads
Deeper granularity
Something entirely new?