## Slide 1: DPC4 Results, Awards, and Closing Remarks
Co-located with HPCA 2026
Organizers: Rahul Bera, Konstantinos Kanellopoulos, and Onur Mutlu
February 1, 2026
Sydney, Australia

## Slide 2: Workloads: 610 Single-Core Traces
Chart: 
| AIML | Google | Graph | SPEC17
Total | 80 | 359 | 79 | 92
Chart: 
| Llama2 | Stable Diffusion | Bark | Whisper | ViT | BioGPT | CLIP | RWKV
 | 25 | 15 | 10 | 8 | 6 | 6 | 5 | 5
Chart: 
| Merced | Yankee | Tango | Tahoe | Sierra.a.4 | Charlie | Sierra.a.6 | Sierra.a.3 | Arizona | Delta | Bravo | Whiskey
Total | 89 | 83 | 51 | 40 | 24 | 22 | 18 | 17 | 6 | 4 | 3 | 2

## Slide 3: Workloads: 484 Random Four-Core Trace Mixes
Chart: 
| AIML | Google | Graph | SPEC17 | Cross-mix
 | 99 | 100 | 91 | 94 | 100

## Slide 4: Baseline
Berti @ L1D and Pythia at L2
  +15.1% in 4800 MTPS and +6.1% in 800 MTPS over no-prefetching
Why? Highest performing combination across the board
  L1D: aggressive stride, IPCP, Berti
  L2: VA-AMPM, SPP, SMS, Pythia
  Configurations: single-core with 4800 MTPS and 800 MTPS

## Slide 5: Scoring Rubric
Every submission is evaluated in three system configurations to receive three scores:
  FullBW score: Non-weighted geomean speedup across 610 traces in single-core with 4800 MT/s DRAM bandwidth
  LimitBW score: Non-weighted geomean speedup across 610 traces in single-core with 800 MT/s DRAM bandwidth
  MC score: Non-weight geomean of harmonic speedup ratio across 484 random four-core mixes in four-core system with 4800 MT/s DRAM bandwidth
Overall score: non-weighted geomean of FullBW score, LimitBW score, and MC score

## Slide 6: Scoring Rubric
Every submission is evaluated in three system configurations to receive three scores:
  FullBW score: Non-weighted geomean speedup across 610 traces in single-core with 4800 MT/s DRAM bandwidth
  LimitBW score: Non-weighted geomean speedup across 610 traces in single-core with 800 MT/s DRAM bandwidth
  MC score: Non-weight geomean of harmonic speedup ratio across 484 random four-core mixes in four-core system with 4800 MT/s DRAM bandwidth
Overall score: non-weighted geomean of FullBW score, LimitBW score, and MC score
Winners are selected based on the overall score

## Slide 7: One Stop for DPC4 Resources
https://github.com/CMU-SAFARI/DPC4

## Slide 8: Surprise Announcement
Monetary award for the winners!
1st Place: $2000
2nd Place: $1500
3rd Place: $1000

## Slide 9: And the Winners Are ...

## Slide 10: Joint 3rd Place - I
“SPPAM: Signature Pattern Prediction and Access-Map Prefetcher”
  Maccoy Merrell, Lei Wang, Paul Gratz, and Savros Kalafatis
  Texas A&M University

## Slide 11: Joint 3rd Place - II
“The Entangling Data Prefetcher”
  Agustin Navarro Torres, Simranjit Singh, Biswabandan Panda, and Alberto Ros
  University of Zaragoza, IIT Bombay, and University of Murcia

## Slide 12: 2nd Place
“Global Berti: Simultaneous Streaming and Spatial Prefetching”
  Gilead Posluns and Mark Jeffrey
  University of Toronto

## Slide 13: Winner of DPC4
“Pushing the Limits of Berti Prefetcher”
  Simranjit Singh, Agustin Navarro Torres, and Alberto Ros
  University of Murcia and University of Zaragoza

## Slide 14: Results – Legend
Abbreviation | Paper
VIP | Crossing the Boundary: Virtual-Address Based Inter-Page Prefetching for Lower Level Caches
SPPAM | SPPAM: Signature Pattern Prediction and Access-Map Prefetcher
Emender | Emender: Optimizing Prefetch Priority and Throttling in VBerti+Pythia
sBerti | sBerti: Enhancing Berti with a Smart Stride Prefetcher for Better Coverage
BertiGO | Pushing the limits of the Berti prefetcher
EDP | The Entangling Data Prefetcher
uMAMA | Performance-Driven Composite Prefetching with Bandits
GBerti | Global Berti: Simultaneous Streaming and Spatial Prefetching

## Slide 15: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035

## Slide 16: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035

## Slide 17: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035
BertiGO is almost consistently the best across all three scores

## Slide 18: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035

## Slide 19: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035
BertiGO, GBerti, and EDP are the only three submissions that outperforms the baseline in all three configurations

## Slide 20: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035

## Slide 21: Results – Score Overview
Chart: Score (higher is better)
| FullBW | LimitBW | MC | Overall
uMAMA | 1.0039 | 0.98608 | 0.98088 | 0.99025
sBerti | 0.99996 | 0.98497 | 1.0023 | 0.99571
baseline | 1 | 1 | 1 | 1
VIP | 1.0226 | 0.98671 | 1.0025 | 1.0038
Emender | 1.033 | 1.0239 | 0.97625 | 1.0107
SPPAM | 1.0201 | 1.0269 | 0.99958 | 1.0155
EDP | 1.0265 | 1.0155 | 1.0058 | 1.0159
GBerti | 1.0262 | 1.0197 | 1.019 | 1.0216
BertiGO | 1.0516 | 1.0257 | 1.0279 | 1.035
SPPAM is the only prefetcher
whose performance gain increases from FullBW to LimitBW

## Slide 22: Results – FullBW Score
Chart: FullBW score (higher is better)
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.1061 | 0.97732 | 1.0199 | 1.0111 | 1.0039
sBerti | 1.0607 | 0.9856 | 1.0025 | 1.003 | 0.99996
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.1916 | 0.9951 | 1.0064 | 1.0094 | 1.0226
Emender | 1.1303 | 1.0096 | 1.0275 | 1.0496 | 1.033
SPPAM | 1.0749 | 0.99816 | 1.0367 | 1.0466 | 1.0201
EDP | 1.0948 | 1.0133 | 1.0225 | 1.0242 | 1.0265
GBerti | 1.0737 | 1.0118 | 1.0298 | 1.0393 | 1.0262
BertiGO | 1.2772 | 1.0113 | 1.0386 | 1.0455 | 1.0516
Most benefiting from prefetching
Least benefiting from prefetching
AIML
Google

## Slide 23: Results – FullBW Score vs. DRAM Requests
Chart: FullBW score
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.1061 | 0.97732 | 1.0199 | 1.0111 | 1.0039
sBerti | 1.0607 | 0.9856 | 1.0025 | 1.003 | 0.99996
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.1916 | 0.9951 | 1.0064 | 1.0094 | 1.0226
Emender | 1.1303 | 1.0096 | 1.0275 | 1.0496 | 1.033
SPPAM | 1.0749 | 0.99816 | 1.0367 | 1.0466 | 1.0201
EDP | 1.0948 | 1.0133 | 1.0225 | 1.0242 | 1.0265
GBerti | 1.0737 | 1.0118 | 1.0298 | 1.0393 | 1.0262
BertiGO | 1.2772 | 1.0113 | 1.0386 | 1.0455 | 1.0516
Chart: Normalized DRAM requests (lower is better)
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.0117 | 1.1161 | 1.129 | 1.0517 | 1.0951
sBerti | 1.0071 | 1.0918 | 1.1203 | 1.0969 | 1.085
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.0084 | 1.0599 | 1.2356 | 1.1188 | 1.0843
Emender | 1.0046 | 0.87749 | 0.97165 | 0.99039 | 0.92227
SPPAM | 1.0021 | 0.84617 | 0.9987 | 1.0196 | 0.91074
EDP | 1.002 | 0.89529 | 0.98574 | 0.99306 | 0.93479
GBerti | 1.0053 | 0.88311 | 1.0635 | 0.98958 | 0.93771
BertiGO | 1.0045 | 0.88172 | 1.0301 | 0.99383 | 0.93294

## Slide 24: FullBW Score per Unit Increase in DRAM Requests
Chart: FullBW score adjusted per unit increase in DRAM requests (higher is better)
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.0932 | 0.87566 | 0.90333 | 0.96138 | 0.91677
sBerti | 1.0532 | 0.90274 | 0.89489 | 0.91439 | 0.92167
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.1817 | 0.93882 | 0.8145 | 0.90224 | 0.94314
Emender | 1.1251 | 1.1505 | 1.0575 | 1.0598 | 1.1201
SPPAM | 1.0727 | 1.1796 | 1.0381 | 1.0265 | 1.1201
EDP | 1.0927 | 1.1318 | 1.0373 | 1.0313 | 1.0981
GBerti | 1.0681 | 1.1457 | 0.96832 | 1.0502 | 1.0944
BertiGO | 1.2715 | 1.147 | 1.0083 | 1.052 | 1.1272

## Slide 25: FullBW Score per Unit Increase in DRAM Requests
Chart: FullBW score adjusted per unit increase in DRAM requests (higher is better)
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.0932 | 0.87566 | 0.90333 | 0.96138 | 0.91677
sBerti | 1.0532 | 0.90274 | 0.89489 | 0.91439 | 0.92167
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.1817 | 0.93882 | 0.8145 | 0.90224 | 0.94314
Emender | 1.1251 | 1.1505 | 1.0575 | 1.0598 | 1.1201
SPPAM | 1.0727 | 1.1796 | 1.0381 | 1.0265 | 1.1201
EDP | 1.0927 | 1.1318 | 1.0373 | 1.0313 | 1.0981
GBerti | 1.0681 | 1.1457 | 0.96832 | 1.0502 | 1.0944
BertiGO | 1.2715 | 1.147 | 1.0083 | 1.052 | 1.1272
Emender, SPPAM and BertiGO provide
the most performance gains for unit DRAM request overhead

## Slide 26: Results – FullBW vs. LimitBW Scores
Chart: FullBW Score
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.1061 | 0.97732 | 1.0199 | 1.0111 | 1.0039
sBerti | 1.0607 | 0.9856 | 1.0025 | 1.003 | 0.99996
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.1916 | 0.9951 | 1.0064 | 1.0094 | 1.0226
Emender | 1.1303 | 1.0096 | 1.0275 | 1.0496 | 1.033
SPPAM | 1.0749 | 0.99816 | 1.0367 | 1.0466 | 1.0201
EDP | 1.0948 | 1.0133 | 1.0225 | 1.0242 | 1.0265
GBerti | 1.0737 | 1.0118 | 1.0298 | 1.0393 | 1.0262
BertiGO | 1.2772 | 1.0113 | 1.0386 | 1.0455 | 1.0516
Chart: LimitBW score
| AIML | Google | Graph | SPEC17 | Overall
uMAMA | 1.0007 | 0.96995 | 1.0294 | 1.0006 | 0.98608
sBerti | 1.0088 | 0.97593 | 0.99729 | 0.98942 | 0.98497
baseline | 1 | 1 | 1 | 1 | 1
VIP | 1.018 | 0.9792 | 0.97654 | 0.99817 | 0.98671
Emender | 1.0241 | 1.0215 | 1.0278 | 1.0297 | 1.0239
SPPAM | 1.0295 | 1.0197 | 1.05 | 1.0328 | 1.0269
EDP | 1.009 | 1.0213 | 1.0127 | 1.0011 | 1.0155
GBerti | 1.0135 | 1.0221 | 1.0214 | 1.0147 | 1.0197
BertiGO | 1.0285 | 1.0215 | 1.033 | 1.0337 | 1.0257
Perf. drops the most from FullBW to LimitBW

## Slide 27: Results – MC Score
Chart: MC score (higher is better)
| AIML | Google | Graph | SPEC17 | Cross-mix | Overall
uMAMA | 1.0108 | 0.97514 | 0.95053 | 0.9799 | 0.98647 | 0.98088
sBerti | 1.0502 | 0.97227 | 0.99743 | 0.99263 | 0.99996 | 1.0023
baseline | 1 | 1 | 1 | 1 | 1 | 1
VIP | 1.0818 | 0.98049 | 0.97804 | 0.97294 | 0.99968 | 1.0025
Emender | 1.007 | 1.0174 | 0.91324 | 0.97629 | 0.96529 | 0.97625
SPPAM | 1.0258 | 1.0213 | 0.92048 | 1.0325 | 0.99705 | 0.99958
EDP | 1.014 | 1.0241 | 0.9863 | 1.0023 | 1.0006 | 1.0058
GBerti | 1.0545 | 1.0249 | 0.98106 | 1.035 | 0.99897 | 1.019
BertiGO | 1.0812 | 1.0205 | 0.97073 | 1.0577 | 1.0102 | 1.0279
All prefetchers struggle
to even match the baseline

## Slide 28: In Conclusion

## Slide 29: Key Highlights of DPC4
8 new prefetching proposals – pushing the limits of the state-of-the-art in various system configurations
  Time for community to start dissecting
482 new ChampSim traces – capturing a wide range of workloads
  Hopefully be useful to posterity

## Slide 30: For the Next DPC ...
HW/SW co-designed prefetcher
  Exposing a rich set of software-level information/hints via ChampSim API
More system-awareness, multi-core awareness, ...
Security-aware prefetcher
Any other suggestions/ideas?

## Slide 31: Acknowledgements
All program committee members
  Akanksha Jain
  Alaa Alameldeen
  Alberto Ros
  Anant Nori
  Biswa Panda
  Leeor Peled
  Mike Ferdman
  Paul Gratz
  Pierre Michaud
Invited speakers
  Akanksha Jain
  Leeor Peled
HPCA 2026 Workshop Chair
  Tom St. John
All HPCA 2026 organizers
All attendees – off-line and online
Organizers and Evaluators
  Konstantinos Kanellopoulos, Onur Mutlu
  Zhenrong Lang

## Slide 32: Thank you for attending DPC4!

## Slide 33: BACKUP

## Slide 34: DPC4 Dinner
Venue: Alegre Bar and Dining
Time: Feb 1, 2026 8PM Sydney
Together with invited speakers from MCCSys workshop
https://events.safari.ethz.ch/hpca26-MCCSys/
https://www.youtube.com/watch?v=3wtg4sTp1qw