## Slide 1: Performance-Driven Composite Prefetching with Bandits
Charles Block, Pedro Palacios Almendros, Abraham Farrell, Gerasimos Gerogiannis, Josep Torrellas
University of Illinois Urbana-Champaign
coblock2@illinois.edu
February 1, 2026

## Slide 2: Prefetching Feedback Mechanisms
Many prefetchers collect feedback to tune their actions
  Pythia and Berti both use accuracy/timeliness information
Complex relationship between heuristics and performance
  Tradeoff between accuracy and coverage changes between workloads
Individual prefetchers struggle to use performance as feedback
  Performance is a very coarse-grained metric
  Prefetchers must make fine-grained decisions (stride offsets, etc.)

## Slide 3: Ensembles of Prefetchers
Extract the benefits of many types of prefetchers
Offers coarse-grained decisions
  Which prefetchers should be active in a workload?
  Which prefetchers should be prioritized?
Performance-driven control becomes feasible
"Arm Neoverse V2 platform", Hot Chips 2023

## Slide 4: Multi-Armed Bandits

## Slide 5: Multi-Armed Bandits
Which machine pays out most?

## Slide 6: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg

## Slide 7: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
3
0
2

## Slide 8: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
3
0
2

## Slide 9: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
3
0
2

## Slide 10: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
1.5
0
2

## Slide 11: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
1.5
0
2

## Slide 12: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
1.5
0
2

## Slide 13: Multi-Armed Bandits
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
1.5
0
2.5

## Slide 14: Micro-Armed Bandit for Prefetching
Images by bizmac - IMG_7080, CC BY 2.0, https://commons.wikimedia.org/w/index.php?curid=54615179; and by Naomi Andrzejeski - https://commons.wikimedia.org/wiki/File:Proof_Coin_-_1_Penny,_Australia,_1949.jpg
1
0
1.5
0
2.5
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS

## Slide 15: Micro-Armed Bandit for Prefetching
1
0
1.5
0
2.5
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS
Stream
Stride
SMS
IPC=2.55

## Slide 16: Micro-Armed Bandit for Prefetching
Gerogiannis & Torrellas, "Micro-Armed Bandit: Lightweight & Reusable Reinforcement Learning for Microarchitecture Decision-Making," Micro 2023

## Slide 17: Micro-Armed Bandit for Prefetching
Gerogiannis & Torrellas, "Micro-Armed Bandit: Lightweight & Reusable Reinforcement Learning for Microarchitecture Decision-Making," Micro 2023

## Slide 18: Micro-Armed Bandit for Prefetching
Gerogiannis & Torrellas, "Micro-Armed Bandit: Lightweight & Reusable Reinforcement Learning for Microarchitecture Decision-Making," Micro 2023

## Slide 19: Micro-Armed Bandit for Prefetching
Gerogiannis & Torrellas, "Micro-Armed Bandit: Lightweight & Reusable Reinforcement Learning for Microarchitecture Decision-Making," Micro 2023

## Slide 20: Micro-Armed Bandit for Prefetching
Gerogiannis & Torrellas, "Micro-Armed Bandit: Lightweight & Reusable Reinforcement Learning for Microarchitecture Decision-Making," Micro 2023

## Slide 21: The Multi-Core Problem

## Slide 22: The Multi-Core Problem
CPU
L2
RL
CPU
L2
RL
CPU
L2
RL
CPU
L2
RL
LLC
Memory
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025

## Slide 23: The Multi-Core Problem
CPU
L2
RL
CPU
L2
RL
CPU
L2
RL
CPU
L2
RL
LLC
Memory
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025

## Slide 24: Aggressiveness Grows with Cores
Most become less aggressive when resources are scarce
Bandit becomes more aggressive when resources are scarce
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025

## Slide 25: Micro-MAMA
We address this with Micro-MAMA
  A central agent supervises the system
  Pushes prefetcher agents towards better system-wide equilibria
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025

## Slide 26: The Micro-MAMA Architecture
Config + Perf
Config + Perf
Config + Perf
Config + Perf
Measure Perf

## Slide 27: The Micro-MAMA Architecture
Measure Perf
Compute System-Level Perf & Update Reward Tables

## Slide 28: The Micro-MAMA Architecture
Measure Perf
Compute System-Level Perf & Update Reward Tables
Choose New Config

## Slide 29: Micro-MAMA
Records joint-actions in a Joint-Action Value Cache
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025
Which action?
How many times?
How performant?

## Slide 30: Micro-MAMA
Records joint-actions in a Joint-Action Value Cache
A Bandit-like Arbiter chooses between
  Letting local prefetcher ensembles act independently
  Enforcing a previously-observed joint action on all local prefetchers
Block et al., "Micro-MAMA: Multi-Agent Reinforcement Learning for Multicore Prefetching," Micro 2025

## Slide 31: A New Reward Function
Ideally, the reward should be the desired performance metric
  In DPC4: harmonic mean of core speedups over 1C Berti+Pythia
However, it is difficult to estimate this at runtime
  How much slower does multicore make this workload?
  How fast would this run if Pythia was used?
We use a simpler reward for Micro-MAMA: Geomean IPC
  We also make this a small part of each local agent's reward

## Slide 32: The Full Prefetcher Selection
L1
L2
LLC
Berti
Next-Line
Stream
Stride
SMS
BOP
"as-is"

## Slide 33: The Full Prefetcher Selection

## Slide 34: Our Arms

## Slide 35: Our Arms
ON/OFF

## Slide 36: Our Arms
Control prefetcher aggressiveness by varying degree

## Slide 37: Performance
AI/ML benefits from very aggressive streaming
Sub-optimal arm selection for Google

## Slide 38: Performance
Underperform the baseline in multicore
  Likely due to limited selection of low-aggressiveness arms

## Slide 39: Multi-Core Benefit of Micro-MAMA
Micro-MAMA improves on Bandit in all MC categories
  Without coordination, local agents over-compete for resources
Global coordination allows better resources sharing and prioritizes workloads with higher sensitivity

## Slide 40: Design Space Exploration
No success at automating arm selection with
  Bayesian optimization (and several similar methods)
  Evolutionary algorithms
Nothing outperformed random search

## Slide 41: Design Space Exploration
No success at automating arm selection with
  Bayesian optimization (and several similar methods)
  Evolutionary algorithms
Nothing outperformed random search
In the end, humans chose which arms to provide to Bandit

## Slide 42: Design Space Exploration
We still believe that automated methods of selecting arms are necessary for achieving Bandit/Micro-MAMA's full potential
Traditional autotuning algorithms are not well-suited to the highly-categorical nature of this problem
Long simulation times (esp. multicore) make iterative processes very time-consuming

## Slide 43: Conclusion
We present a performance-driven L2 prefetching solution using multi-armed bandit models for ensemble control
System-level control like Micro-MAMA is crucial for these systems to perform well in multicore
Design space exploration for these systems remains challenging and an interesting future research direction

## Slide 44: Performance-Driven Composite Prefetching with Bandits
Charles Block, Pedro Palacios Almendros, Abraham Farrell, Gerasimos Gerogiannis, Josep Torrellas
University of Illinois Urbana-Champaign
coblock2@illinois.edu
February 1, 2026